## Slide 1: Uncertainty Quantification with the SimCenter quoFEM application
Francisco Galvis
Adam Zsarnóczay

## Slide 2: Motivation
Calibrate numerical models and quantify the uncertainty in their outputs.
Column lateral drift ratio history
Table acceleration input history
Full-size bridge column tested at the outdoor shake table at UC San Diego
Measured responses (displacements, accelerations, and reactions) compared to blind-predictions from numerical analyses
Predictions vs. Experiments
source: PEER Report 2015/01 https://www.youtube.com/watch?v=FAeeHh_y3u0

## Slide 3: Motivation
Calibrate numerical models and quantify the uncertainty in their outputs.
Structural Health Monitoring system in One Rincon Tower records building response to earthquakes and ambient motions
System Identification is used to characterize the vibration and damping in the building
source: Celebi, Hooper, and Klemencic (2017)
doi: https://doi.org/10.1193/031616EQS041M

## Slide 4: Motivation
quoFEM is a desktop application developed to connect state-of-the-art UQ engines with computational simulation tools
UQ engines
simulation tools

## Slide 5: Motivation
Today’s class:
quoFEM is a desktop application developed to connect state-of-the-art UQ engines with computational simulation tools

## Slide 6: Before we get started
Online documentation: nheri-simcenter.github.io/quoFEM-Documentation/index.html
Installation instructions: documentation: user manual/installation
Message board: simcenter-messageboard.designsafe-ci.org/smf/index.php

## Slide 7: Before we get started - Installation

## Slide 8: Before we get started – SimCenter Forum

## Slide 9: quoFEM workflow

## Slide 10: Before we get started – Loading input files

## Slide 11: Before we get started – If something goes wrong…

## Slide 12: What can we do with quoFEM?
1) Parametric Study
Explore the response surface
Formulate an objective function for calibration
2) Conventional Calibration
Optimize to minimize error;
One deterministic result
3) Bayesian Calibration
Solve the inverse problem: distribution of params | distribution of reference results
4) Forward propagation
Propagate uncertainty in parameters to uncertainty in outputs

## Slide 13: Objective functions
input parameter
response quantity (e.g., force)
model
target / reference
difference ~ error

## Slide 14: Objective functions
input parameter
error measure a.k.a. objective function
response quantity (e.g., force)
difference ~ error
difference ~ error
input parameter
model
target / reference

## Slide 15: Objective functions
figure source: Wikipedia
input parameter
input parameter
error measure a.k.a. objective function
Sphere function:
global minimum

## Slide 16: Objective functions
figure source: Wikipedia
input parameter
input parameter
error measure a.k.a. objective function
Rosenbrock function:
a = 1
b = 100
global minimum

## Slide 17: Objective functions
input parameter
error measure a.k.a. objective function
response quantity (e.g., force)
difference ~ error
difference ~ error
input parameter
model
target / reference
???

## Slide 18: Objective functions
figure source: Wikipedia
input parameter
input parameter
error measure a.k.a. objective function
Rosenbrock function:
a = 1
b = 100
global minimum f(x,y) = 0
A small mistake in the error can lead to a large uncertainty in the calibrated parameters
f(x,y) = 2.25
f(x,y) = 2.25

## Slide 19: Example 0 – Rosenbrock function
The quoFEM tool can run any Python script, that returns one or more error measures.
source: Wikipedia

## Slide 20: Example 0 – Rosenbrock function
The quoFEM tool can run any Python script, that returns one or more error measures.
rosenbrock.py
source: Wikipedia

## Slide 21: Example 0 – Rosenbrock function
The quoFEM tool can run any Python script, that returns one or more error measures.
rosenbrock.py
params.py
source: Wikipedia
calculation
print output

## Slide 22: Example problem in OpenSeesPy
Parameter calibration for a concentrated plasticity column
Cantilever column model
https://nisee.berkeley.edu/spd/index.html
~400 tests of RC column tests

## Slide 23: Example problem in OpenSeesPy
Parameter calibration for a concentrated plasticity column
Cantilever column model
Soesianawati, 1989

## Slide 24: Example problem in OpenSeesPy
What are the model parameters to simulate the behavior of this column using a plastic hinge model?
Soesianawati, 1989
Rotation [rad]
Moment
Mp
c
r
Kspr
Symmetric backbone of the rotational springs
Mr
Onset of degradation
Mc
E

## Slide 25: Example problem in OpenSeesPy
Calibrate elastic properties and relevant plastic hinge parameters
run_analysis.py file provides a starting point:
Clean and open model
Define constants
Define materials
Create nodes
Assign supports
Create elements
Define lateral load
Run cyclic analysis
(takes about 2 s per iteration)
you’ll need to run hundreds of iterations

## Slide 26: What can we do with quoFEM?
1) Parametric Study
Explore the response surface
Formulate an objective function for calibration
2) Conventional Calibration
Optimize to minimize error;
One deterministic result
3) Bayesian Calibration
Solve the inverse problem: distribution of params | distribution of reference results
4) Forward propagation
Propagate uncertainty in parameters to uncertainty in outputs
source: Wikipedia
input
input
error
error
input
input

## Slide 27: Example 1 – Parametric study
What is a reasonable range for the expected inputs?
What is the possible domain of error fitting the force history?
input
input
input
500 simulations
Rotation [rad]
Moment
Mp
0.10
Kspr
Mc
Objective function:

## Slide 28: Example 1 – Parametric study

## Slide 29: Example 1 – Parametric study

## Slide 30: Example 2 – Optimization (Conventional Calibration)
Convergence path using deterministic calibration
12 simulations

## Slide 31: Example 3 – Bayesian Calibration
What are the plausible additional parameters that could give a reasonable prediction?
from the parametric study:
Bayes’ rule:
= prior
= posterior
= likelihood function
= evidence (data)

## Slide 32: Example 3 – Bayesian Calibration
What are the plausible additional parameters that could give a reasonable prediction?
7500 model evaluations
Deterministic calibration
Mean

## Slide 33: What can we do with quoFEM?
1) Parametric Study
Explore the response surface
Formulate an objective function for calibration
2) Conventional Calibration
Optimize to minimize error;
One deterministic result
3) Bayesian Calibration
Solve the inverse problem: distribution of params | distribution of reference results
4) Forward propagation
Propagate uncertainty in parameters to uncertainty in outputs

## Slide 34: Module No. 2
Repeat the steps shown in examples 1 – 3 on a different experiment from the same research project (Higher axial load).
Input files, detailed description and submission guidelines to be posted on Canvas